## Slide 1: LCA Decision Tool
University of Rostock
Sven Mauch, Julian Wiechert, Ibrahim Rahmouni

## Slide 2: Content
In the following slides the concept of the Decision Tool will be presented
For reasons of clarity, the ecological and economic approaches are presented separately.
For the final implementation, both approaches are implemented in one tool
Please provide us your feedback! 

## Slide 3: Environmental Model Concept
Time horizon in years
LCLFG Flow at year 1
CH4 content at year 1
Year 1
Year 2
Year 3
Year 4
Year 1
Year 2
Year 3
Year 4
machine utilisation [%]
Operating Supply
Oil
Diesel
O2
…
Gas processing
machine production
Model parameters affected by Volume Flow and CH4 content
Other parameters
Year 1 results
Year 2 results
Year 3 results
Year 4 results
Sum of results
Input parameters (adjustable)
Iteration Cycle
Iteration results / Output parameters

## Slide 4: Input Parameters
3 Input - parameters have been identifyed as most important:
  LCLFG volume flow at year 1 – defines the amount of Gas that the landfill emits at the beginning of the observed time horizon
  CH4 content at year 1 – defines the content of CH4 in the landfill gas at the beginning of the observed time horizon
  Time horizon – defines the lenght of the observed period
LCLFG Flow
  Directly impacts the following model parameters
    machine capacity utilisation, use of operating resources (oil etc.), maintenance resources (use of filters etc.)
    Gas processing: How much energy is produced; Qantity and quality of emissions
Ch4 content
  Directly impacts the following model parameters
    Use of operating resources: How much Diesel (DFE), Oxygen enriched gas (OER), chemical fluid (SFR) is necessary ?
    Gas processing: How much energy is produced; Qantity and quality of emissions
Time horizon:
  LCLFG volume flow and CH4 content are a function of the time horizon
    Beginning with the input value for year 1 the tool will approximate the developement over the time horizon based on a backed model
  A manual input option to adjust the input variables based on the time horizon can be implemented

## Slide 5: Calculation Method – 3 Phases of calculation
  Phase 1: LCA base scenario
    Calculation of a base scenario with Open LCA based on Ecoinvent data for every sub step of a process:
      E.g. Dual Fuel Engine: Impacts for machine production, Diesel production, machine oil use, gas processing etc.
    These base scenarios will be calculated for a 100 % machine use
      A predefined LFG volume flow has to be considered
      A predefined CH4 content of the gas will be considered
    The results will be exported (no need to access Ecoinvent database or openLCA will be necessary)
  Phase 2: Relation between base scenario and model Input parameters
    The results will be calculated based on the relation of the input parameters to the process
      E.g.: Volume flow 50% higher than in base scenario → machine use 50% higher → oil use 50% higher → Environmental impact results of oil increase by 50% (only exemplary – probably not linear)
    It will be important to understand the real relation between the input parameters and the sub processes of the model
  Phase 3: Iteration on Time horizon
    Phase two will be repeated in a loop calculation for every year of the time horizon
    The change of volume flow and Ch4 content will be taken into account in this way
    The final results will be the sum of the results of each iteration step and will be presented for each technology

## Slide 6: Result parameters
3 Types of result parameters :
  Amount of usable energy:
    Important for the economic calculation
    Important for the calculation of CO2 benefits compared to the base scenario (flare)
  Amount of emitted CO2 equivalents
    Important for the calculation of CO2 benefits compared with the base scenario
    May impact economical consideration
  Other emissions to the environment:
    Can be based on LCIA evaluation models like the following:
      ReCiPe Methodology: 18 Midpoint Impact indicators like accidification, eco toxicity, raw material use … ; it is possible to use endpoint categories
      Environmental Footprint (EF) Methodology: Recommended by ILCD (International Reference Life Cycle Data System) by the European Union. 25 midpoint categories

## Slide 7: Questions to the Environmental model concept?
Please note your remarks and questions:
Do you recommend to consider other input parameters than the previously mentioned ones?
  E.g. more adjustable parameters to characterize the landfill , include the use time of the machine as input parameter
Do you think the calculation method is consistent?
Do you have any recommendations for result parameters?
Your remarks:
…

## Slide 8: Economical Model Concept
CO2 emissions
Usable Energy
Amortisation
Environmental Model Inputs and Results
Country
Energy price
Time horizon
Turnover
CO2 price (yes/no)
Co2 price
CO2 savings to baseline
Operating costs
Machine Investment
Profit after tax
Cash flow
i
investment
Input
Result
Model parameters
Profit befor tax
taxes

## Slide 9: Economic model – calculation method
The aim of the economic model is to calculate the NVP (Net present Value)
Input Parameters
  The model uses two Input sources:
    The results of the environmental model for energy production and CO2 compensation (compared to baseline) as well as the input for the time horizon
    Extra inputs that the user can define: Energy price and country
Model Parameters
  The turnover is calculated based on the income from energy and CO2 and the operating costs
  The profit is calculated based on the turnover and the amortisation rate (country specific)
  The investment costs are based on the investment for the machine
  The period i in the NVP formula is directly defined by the time horizon defined as input parameter
  The Calculation interes rate r has to be predefined (could also be Input parameter)

## Slide 10: Questions to the Econimical model concept?
Please note your remarks and questions:
Do you recommend to consider other input parameters than the previously mentioned ones?
  E.g. more adjustable parameters to characterize amortisation, calculation interest rate, etc.?
Do you think the calculation method is consistent?
Do you have any recommendations for result parameters?
  Other economical variables than the NVP?
Your remarks:
…

## Slide 11: THANK YOU FOR ATTENTION
The works was co-financed under the Interreg South Baltic Programme 2021 – 2027 in the Low Calorific Gas for Green Power Production project, project number: STHB.02.01-IP.01-0011/23, https://locagas.eu
Do you have any question?